## Slide 1: Push an AI model to a microcontroller from the cloud, in seconds
One-hour hands-on: vision AI on the EK-RA8P1 with /IOTCONNECT
60-minute hands-on | Presenter Name, Title
Notes: Welcome. Plug in now: Ethernet first, then USB-C to DEBUG1. The boards are already provisioned, so they connect to the cloud while we talk. Everyone should have a board, an LCD, two cables and a seat card; the seat number on the card matches the sticker on the board. The Wi-Fi details and the console URL are on the whiteboard. Ten minutes of talking, forty-five at your board, five to close.

## Slide 2: What you will do in the next hour
FIND
Your board, online
Sign in, open the dashboard with your seat number, and watch your board's live telemetry arrive.
PUSH
Change what it does
Deploy three different AI models from the cloud: a face detector, a 1000-class classifier, an occupancy sensor.
PROVE
Nothing rebooted
Watch uptime keep counting through every swap, then pull the power and see the model come back from flash.
Talk 10
Lab A · 5
Lab B · 15 min
Lab C · 15 min
Talk 7
Close 8
Black is a talk, green is you at your board. Every lab ends at a checkpoint.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Three outcomes. Find: the board is already provisioned, so your job is to find it in the cloud and confirm it is alive. Push: the same board becomes a face detector, then an ImageNet classifier, then an occupancy sensor, purely by deploying models from AI Model Management. Prove: uptime never resets, and after a power cycle the board boots straight into the model you chose. The strip is the hour. Ten minutes of me, forty-five of you.

## Slide 3: What is on your desk
The board
EK-RA8P1 with the camera on J35 and the LCD attached. Flashed and provisioned already: it connects to your device in the cloud by itself. The sticker is your seat number.
Two cables
Ethernet from the board to the drop at your seat. USB-C from your laptop (or the USB power adapter) to DEBUG1: that powers the board.
The seat card
Seat number, your Device ID, the name of your dashboard, and your /IOTCONNECT login. That is all you need today.
Your laptop
A browser for console.iotconnect.io. Optional: a serial terminal at 230400 baud on the board's USB port shows the log lines as models arrive.
One rule all hour: power-cycle, never RESET. A warm reset leaves the LCD white while everything else keeps running.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Point at each item. The boards were provisioned before the session, so nobody types a certificate today. USB-C powers the board; the serial console on the same port is optional and only for people who want to see the log. The seat card is the source of truth: device ID, dashboard name, login.

## Slide 4: Why run vision AI on a microcontroller
No Linux, no MPU
One chip boots in milliseconds, runs deterministic firmware and has no operating system to patch. Camera, NPU, network and display on a Cortex-M85.
Milliwatts and dollars
Always-on sensing at a bill of materials and a power budget an application processor cannot reach. The Ethos-U55 does a face detection in under 6 ms.
But models change
The detector you ship today is retrained next quarter. Updating it must not mean a truck roll, a debugger or a full firmware release.
So the question for today: how do you ship a new model to a fleet of these, and know it took?
EK-RA8P1 · /IOTCONNECT workshop
Notes: The first two cards are the usual case for edge AI on an MCU. The third is why we are here. A model is not firmware: it changes on a different cadence, owned by a different team, and it is a data file. If updating it means a firmware release and a reflash, the model never gets updated. Today you will treat the model as a managed asset in the cloud, push it, and watch the device swap it in while it keeps running.

## Slide 5: The board: Renesas EK-RA8P1
Part | What it is
MCU | RA8P1, Arm Cortex-M85 at 1 GHz
NPU | Arm Ethos-U55, 256 MACs per cycle
Memory | 1 MB MRAM code, 2 MB SRAM, 64 MB SDRAM
Storage | 64 MB OSPI flash: credentials and the model slot
Network | Gigabit Ethernet
Camera | OV5640 over MIPI CSI-2, 55 fps
Display | 7-inch parallel LCD, optional
Debug | On-board J-Link; USB-C DEBUG1 is also the console
EK-RA8P1 · /IOTCONNECT workshop
Notes: The numbers that matter today. One megabyte of code flash: this image has no built-in model, so the first model your board runs will come from the cloud. Sixty-four megabytes of external flash: that is where the credentials and your pushed model live, and why both survive a power cycle. The NPU does the inference; the M85 does everything else. Four threads: camera, inference, display, network. The network thread holds an MQTT session to /IOTCONNECT and that is where the push arrives.

## Slide 6
Click Deploy in AI Models. The board downloads the model, validates it, swaps it in between two inferences and saves it to flash.
No reflash. No reboot. Uptime uninterrupted. It comes back after a power cut.
Notes: Say it once, plainly, then do it for real in Lab B. The claim is checkable on three widgets: the Uptime tile never resets, the Model Source card says cloud and then flash, and the inference-time chart steps as the model changes.

## Slide 7: What happens when you click Deploy
1
Deploy
AI Models sends a command over MQTT carrying a signed download URL.
2
Download
HTTPS from S3 into a 4 MB pending buffer in SDRAM, three retries on error.
3
Validate
Envelope header: magic, length, CRC32. Then a trial load checks the input shape.
4
Hot-swap
Between two inferences: tear down the interpreter, rebuild it over the same arena.
5
Persist
The envelope is written to a raw OSPI flash slot and reloaded at every boot.
A failure at step 3 or 4 keeps the previous model running. The camera, display and telemetry never stop during any step.
A push during a live video stream is deferred until the download can share the heap, then proceeds with the stream still playing.
EK-RA8P1 · /IOTCONNECT workshop
Notes: The mechanism, in one pass, before you do it. One: the deploy is an ordinary cloud-to-device command on the MQTT session the board already holds, with a pre-signed URL. Two: a second TLS session downloads the file into SDRAM, not into the running model's memory. Three: the envelope is checked, magic, length, CRC, and a trial load reads the input tensor shape to decide which family the model is. Four: the inference thread swaps between two frames: destroy the interpreter, construct a new one over the same arena. Five: the file goes to a raw slot in external flash and is read back at boot. Any failure leaves the previous model running.

## Slide 8: Lab A: Find your board in the cloud (5 min)
Board plugged in: Ethernet, then USB-C. Give it 30 seconds.
Sign in at console.iotconnect.io with the login on your seat card.
Open Dashboards and pick the one named with your seat, for example Seat 07.
Confirm the values on the right. Your board is talking to the cloud.
Optional: a serial terminal at 230400 on the board's USB port shows the log.
WHAT YOUR DASHBOARD SHOWS RIGHT NOW
Widget | Value
Device status | Connected
Camera FPS | 55
Uptime (s) | counting up
Active Model | empty: no model yet
NPU Inference Time | 0: inference is idle
Checkpoint: your dashboard shows Connected, Camera FPS 55 and Uptime counting. Inference at zero is expected: you push the first model next.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Gate here: nobody starts Lab B until their dashboard shows Connected and Camera FPS at 55. A board that is not connected after two minutes gets swapped for a spare immediately; helpers carry them. No debugging at the seat in a one-hour format. Inference at zero is expected: the boards arrive with no model.

## Slide 9: Lab B: Your first push (15 min)
1 Deploy Face Detect
AI Models, open RA8P1 Face Detect, choose Deploy, select your device (ek-ra8p1-NN) only, and dispatch.
2 Watch it land
Within seconds: Active Model reads face-v3, Model Source says cloud, NPU Inference Time about 5,800 µs. Step in front of the camera: FACE DETECTED, boxes on the LCD.
3 Take Snapshot
Press Take Snapshot on the dashboard. About 10 seconds later the Latest Snapshot widget shows the photo with the box drawn on it.
IF YOU HAVE THE SERIAL CONSOLE OPEN, THIS IS WHAT ARRIVES
IOTC: model downloaded (441248 bytes)
FD: hot-swapping to model "face-v3" v3 (441088 bytes)
FD: model "face-v3" v3 (cloud, 441088 bytes) loaded: face detector, ethos-u: yes
FD: model persisted to OSPI flash store
Checkpoint: Active Model reads face-v3, inference is about 5,800 µs, Uptime never reset, and a snapshot with a box around your face is on your dashboard.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Do it on the big screen first with your own board: AI Models, Face Detect, Deploy, pick the presenter device, dispatch, and let the room watch the dashboard change. Then let them go. Deploy to your own device only: check the device ID in the dialog before you click. The snapshot is worth a sentence: the board draws the boxes, PNG-encodes the frame and signs the S3 upload itself on the microcontroller. When most of the room has a box on a face, move to Lab C.

## Slide 10: The model library, registered and ready to deploy
In AI Models | What the board becomes | Input | Inference | Size
RA8P1 Face Detect | Face detector with boxes (YOLO Fastest) | 192×192 gray | 5.8 ms | 441 KB
RA8P1 Person Detect | Occupancy sensor: person present or absent | 96×96 gray | 1.5 ms | 240 KB
RA8P1 ImageNet Classifier 0.25 | 1000-class classifier, speed tier | 224×224 RGB | 4.5 ms | 432 KB
RA8P1 ImageNet Classifier 0.5 | 1000-class classifier, mid tier | 224×224 RGB | 9 ms | 1.1 MB
RA8P1 ImageNet Classifier v2 | 1000-class classifier, accuracy tier | 224×224 RGB | 40 ms | 3.1 MB
The camera delivers a frame every 18 ms. Every model here is faster than that: the NPU is never the bottleneck, even at 40 ms with frame skipping.
Classifier v2 is roughly seven times the face detector's size and workload. That is the one to push while you watch the inference chart.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Five models, three tasks, one firmware. The names in the first column are exactly what you see in the deploy list. Inference times are measured on this hardware; the spread from one and a half milliseconds to forty is what makes the inference-time chart on the dashboard interesting. Classifier v2 is the one to push first in Lab C: seven times the face detector, absorbed live.

## Slide 11: Lab C: Re-task the device, then prove it (15 min)
C1
Deploy ImageNet Classifier v2 (3.1 MB). Hold up a mug, a banana, a bottle. The inference chart steps to about 40 ms. Uptime keeps counting.
C2
Deploy Person Detect. Walk out of frame and back. PERSON PRESENT, NO PERSON, inference about 1.5 ms.
C3
Send Model Info from the dashboard. The acknowledgment names the model, version, source and size.
C4
Unplug USB, count to three, plug it back in. About 30 seconds later the board is back, running the same model, Model Source now says flash.
C5
Deploy Face Detect again. The boxes come back. Time left? Push the 0.25 and 0.5 classifiers and compare the chart.
WATCH, ON THE DASHBOARD
Active Model mobilenet-v2
Model Source cloud
Inference 40,000 us
-- after the power cycle --
Active Model person-detect
Model Source flash
Uptime restarts from 0
Model Source changing from cloud to flash after the power cycle, the inference chart stepping with every push, and an Uptime tile that never went to zero during the swaps.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Push the classifier on your own board first and hold up a mug on the big screen, then let them go. Confidence between thirty and sixty percent is a softmax over a thousand classes; the label being right is the point. Single objects, centred, close to the lens. Do C4 together as a room: everybody unplugs, counts to three, plugs in, and watches Model Source change to flash. That is the applause moment. Model Revert clears the stored model rather than restoring a built-in one; after a revert inference idles until the next push.

## Slide 12: Three numbers that prove it
7×
larger model, absorbed live
Face detector at 5,800 µs to Classifier v2 at 40,000 µs, downloaded and swapped while the camera and display kept running.
0
reboots across every swap
The Uptime tile counts through the whole lab. The only time it resets is the power cycle you chose to do.
3
tasks, one firmware image
Face detection, occupancy sensing, 1000-class classification. The family is chosen by the model's input shape, not by a build flag.
And after the power cycle: the same model, from the board's own flash, in about 30 seconds, with no console attached.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Close Lab C with this once most of the room has done the power cycle. Each number is something they saw on their own dashboard in the last half hour. The seven-times figure is the workload jump between the face detector and Classifier v2. Zero reboots is the Uptime tile. Three tasks is the same firmware that was flashed before the session. Every board in this room did this at the same time from the same AI Models entry: that is what fleet rollout looks like.

## Slide 13: Bring your own model, and where to go next
1
Quantize
Export an int8 TensorFlow Lite model whose input matches one of the three contracts.
2
Compile with Vela
Target ethos-u55-256. If Total SRAM used exceeds 640 KiB, recompile with the Size optimisation.
3
Pack
tools/pack_model.py wraps it in the IOTV envelope and writes the STORED zip.
4
Upload and push
AI Models, Create Model, Variant Renesas, upload the zip. Deploy to one device, then to the fleet.
WHERE TO GO NEXT
Quickstart
Repeat today at home on your own trial account, from unboxing, with the prebuilt image and no toolchain.
Developer Guide
Build from source with e² studio and FSP, the thread architecture, the memory budget, adding models.
The repository
github.com/avnet-iotconnect/iotc-freertos-ek-ra8p1: firmware, prebuilt image, template, dashboard, models, workshop.
EK-RA8P1 · /IOTCONNECT workshop
Notes: The path from your own network to a deploy button: quantize to int8 with one of the three input shapes, compile with Vela for the 256-MAC Ethos-U55, wrap it with the thirty-line pack_model.py, upload under AI Models, deploy. The three cards at the bottom are where to go next; the repository holds all of it, including these workshop materials and the full two-and-a-half-hour version with provisioning and live video.

## Slide 14: Before you leave
The board stays here
In the serial console type erase, then reboot. The board forgets its identity. Leave it, the cables and your seat card on the desk.
The board goes home with you
Leave it as it is. The workshop account closes after the event, so follow the Quickstart to make your own, then erase, reboot and provision it again.
Thank you. You pushed three models to a microcontroller today, and it never rebooted.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Say which card applies before anyone stands up. If boards are collected, the erase matters only if attendees opened a console; otherwise the facilitator erases later. If boards go home, remind people the account is temporary and the Quickstart covers making their own. Collect seat cards; they carry a login.

## Slide 15
Notes: Questions. The repository URL is on the whiteboard; the full workshop, the quickstart and the developer guide are all in it.