## Slide 1: Push an AI model to a microcontroller from the cloud, in seconds
Hands-on workshop: vision AI on the EK-RA8P1 with /IOTCONNECT
2 h 30 min hands-on | Presenter Name, Title
Notes: Welcome. While people settle: everyone should have a board, an LCD, a USB-C cable, an Ethernet cable and a printed seat card. The seat number on the card must match the sticker on the board. Wi-Fi details and the two URLs are on the whiteboard. Today is hands-on: about 40 minutes of talking, the rest is you and your board. The one thing we are here to experience: a model pushed from the cloud to a microcontroller, live, without a reflash and without a reboot.

## Slide 2: What you will do today
CONNECT
Make a board yours
Provision an EK-RA8P1 over its serial console and watch it appear in /IOTCONNECT with live telemetry.
PUSH
Change what it does
Deploy three different AI models from the cloud: a face detector, a 1000-class classifier, an occupancy sensor.
PROVE
Nothing rebooted
Watch uptime keep counting through every swap, then pull the power and see the model come back from flash.
Talk 20
Labs 1 to 4 · 55 min
Break
Talk 10
Labs 5 and 6 · 40 min
Talk 15
Black is a talk, green is you at your board. Every lab ends at a checkpoint.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Three outcomes, in order. First you connect: the board becomes your device in the cloud. Second you push: the same board becomes a face detector, then an ImageNet classifier, then an occupancy sensor, purely by deploying models. Third you prove it: uptime never resets, and after a power cycle the board boots straight into the model you chose. The first push happens before the break, so by the time we get coffee everyone has already done the headline thing.

## Slide 3: What is on your desk
The board
EK-RA8P1 with the OV5640 camera on J35 and the 7-inch LCD attached. Already flashed with the workshop firmware. The sticker is your seat number.
Two cables
USB-C from your laptop to DEBUG1: that one cable is power and the serial console. Ethernet from the board to the drop at your seat.
The seat card
Seat number, your board's MAC address, your Device ID, your /IOTCONNECT login, and the account's ENV and CPID. Everything you will type comes from it.
Your laptop
A serial terminal at 230400 baud, a browser for console.iotconnect.io, and a plain-text editor for two certificate files. Not Word.
Two rules all day: power-cycle, never RESET (a warm reset leaves the LCD white), and paste the certificate and the key separately.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Point at each item. The USB-C cable does double duty: power and the console, through the on-board J-Link. The Ethernet is the board's own path to the cloud; your laptop can be on Wi-Fi. The seat card is the source of truth for everything typed today, and the MAC on it exists because every board here was flashed with its own address. The LCD's timing controller only initialises from a cold start, so a warm reset leaves the screen white while everything else keeps running; and the board's paste buffer takes one PEM block at a time.

## Slide 4: Why run vision AI on a microcontroller
No Linux, no MPU
One chip boots in milliseconds, runs deterministic firmware and has no operating system to patch. Camera, NPU, network and display on a Cortex-M85.
Milliwatts and dollars
Always-on sensing at a bill of materials and a power budget an application processor cannot reach. The Ethos-U55 does a face detection in under 6 ms.
But models change
The detector you ship today is retrained next quarter. Updating it must not mean a truck roll, a debugger or a full firmware release.
So the question for today: how do you ship a new model to a fleet of these, and know it took?
EK-RA8P1 · /IOTCONNECT workshop
Notes: The first two cards are the usual case for edge AI on an MCU. The third card is why this workshop exists. A model is not firmware: it changes on a different cadence, owned by a different team, and it is a data file, not code. If updating it means a firmware release and a reflash, the model never gets updated. What you will see today is the alternative: treat the model as a managed asset in the cloud, push it, and have the device swap it in while it keeps running.

## Slide 5: The board: Renesas EK-RA8P1
Part | What it is
MCU | RA8P1, Arm Cortex-M85 at 1 GHz
NPU | Arm Ethos-U55, 256 MACs per cycle
Memory | 1 MB MRAM code, 2 MB SRAM, 64 MB SDRAM
Storage | 64 MB OSPI flash: credentials and the model slot
Network | Gigabit Ethernet
Camera | OV5640 over MIPI CSI-2, 55 fps
Display | 7-inch parallel LCD, optional
Debug | On-board J-Link; USB-C DEBUG1 is also the console
EK-RA8P1 · /IOTCONNECT workshop
Notes: The numbers that matter today. One megabyte of code flash: that is why this image has no built-in model, the flash budget went to the video stack, and the first model you run will come from the cloud. Sixty-four megabytes of external flash: that is where your credentials and your pushed model live, and why both survive a power cycle. The NPU does the inference; the M85 does everything else, including software H.264 for the video lab. The same USB-C port is the debugger and the serial console.

## Slide 6: What the firmware does
VISION PIPELINE, ON THE CHIP
Camera
OV5640, MIPI CSI-2, 55 fps into SDRAM
Preprocess
Crop and convert to the model's input shape
NPU inference
TensorFlow Lite Micro on the Ethos-U55; the model is hot-swappable
Display
Boxes and labels over the live view at 29 fps
NETWORK THREAD, TO /IOTCONNECT
Telemetry
every 10 s over MQTT with mutual TLS
Commands
snapshot, model-info, set-interval, reboot
Model push
HTTPS download, validate, hot-swap, persist
Snapshot
annotated PNG, SigV4-signed upload to S3
Video
software H.264 over WebRTC, one viewer
Storage on the 64 MB OSPI flash: a LittleFS volume for the cloud identity and a raw 8 MB slot for the active model. Both are read back at boot, which is why credentials and the pushed model survive a power cycle.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Four FreeRTOS threads. The top row is the vision pipeline and it runs whether or not the cloud is reachable. The middle row is the network thread and everything it does for /IOTCONNECT. The highlighted card is today's subject: a model push arrives as a command, the file is downloaded over HTTPS, validated, swapped into the inference thread between two frames, and written to flash. The last line is the reason both your credentials and your model survive power loss.

## Slide 7: /IOTCONNECT in one slide
Template
Describes a kind of device: the attributes it reports, the commands it accepts, and whether it may upload files and stream video. Ours is RA8P1 Vision AI.
Device
One identity: a Unique ID plus an X.509 certificate and key. The board presents the certificate over mutual TLS; there are no passwords.
Telemetry and commands
Device to cloud every 10 seconds; cloud to device on demand, each acknowledged. MQTT over TLS on port 8883.
Dashboard
Widgets bound to one device's attributes and commands. You import a ready-made one and bind it to your device.
AI Models
Register a model file once, version it, and deploy it to any device on a compatible template. The device does the rest.
Telemetry Files
Files the device uploads, such as the annotated snapshot. The board signs the S3 upload itself with temporary AWS credentials.
EK-RA8P1 · /IOTCONNECT workshop
Notes: The vocabulary for the labs. Template is already imported, so you only pick it from a list. Device is what you create in Lab 2, and the certificate you download there is what you paste into the board in Lab 3. Dashboard is Lab 4a. AI Models is the highlighted card and the point of the day: the five models are already registered; you deploy them. Telemetry Files is where the snapshot ends up. The template turns on video streaming, and the platform provisions the video channel at the moment the device is created, so use exactly this template.

## Slide 8
Click Deploy in AI Models. The board downloads the model, validates it, swaps it in between two inferences and saves it to flash.
No reflash. No reboot. Uptime uninterrupted. It comes back after a power cut.
Notes: Say it once, plainly, then do it for real in Lab 4. The claim is checkable on three widgets: the Uptime tile never resets, the Model Source card says cloud and then flash, and the inference-time chart steps as the model changes. Everything after the break is about how each step of this sentence is implemented.

## Slide 9: The lab flow
Lab | Name | What you do | Checkpoint | Min
1 | Meet your board | Console at 230400, confirm MAC and IPv4 | Camera at 55 fps, network up | 10
2 | Claim your device | Create a device from the RA8P1 Vision AI template | Certificate and key downloaded | 10
3 | Provision the board | set env, cpid, duid; paste cert and key; apply | IOTC: connected | 15
4 | Dashboard, first push, snapshot | Import the dashboard, deploy Face Detect, Take Snapshot | A snapshot with a box on it | 20
5 | Re-task the device | Classifier, person detector, model-info, power-cycle | Model reloads from flash | 30
6 | Live video | Start Video, then push a model mid-stream | Stream stays up through the swap | 10
Each lab ends at a checkpoint. Do not move on until you have seen it; raise your seat card and a helper will come to you.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Leave this slide up while people start Lab 1. The gates are real: Lab 1 catches every driver, cable and network problem early, when a helper has time to fix it. Lab 3 is the slow one, so the break comes after Lab 4 rather than after Lab 3, and everyone gets their first push before coffee. Helpers: the checkpoint column is what you are looking for on each screen as you sweep.

## Slide 10: Lab 1: Meet your board (10 min)
Camera seated on J35, LCD cables seated.
Ethernet to your drop. USB-C to DEBUG1.
Serial terminal: 230400, 8N1, line ending CR.
Press Enter, then type help.
Find the MAC line. Compare it with your seat card.
ON THE CONSOLE
Network up (DHCP):
MAC : 02:8a:9b:57:53:07
IPv4 : 192.168.10.57
Processing time:
Camera vsync period : 18 ms, 55 fps
AI inference (U55) : 0 us, 0 fps
IOTC: no credentials provisioned
FD: no built-in model and no stored model
Checkpoint: the MAC matches your card, an IPv4 address was assigned, the camera runs at 55 fps. Inference at zero is expected: there is no model yet.
EK-RA8P1 · /IOTCONNECT workshop
Notes: The two settings that catch most people: 230400 baud, not 115200, and the terminal must transmit a carriage return, or the board never sees a command. Tera Term: Setup, Terminal, New-line Transmit: CR. Mac and Linux: screen on the usbmodem device at 230400. The MAC check matters: every board here was flashed with its own address, and two boards with the same MAC on one switch would fight each other; if the console and the card disagree, get a helper. Inference reads zero because this image has no compiled-in model; the first one comes from the cloud in Lab 4.

## Slide 11: Lab 2: Claim your device in /IOTCONNECT (10 min)
Sign in at console.iotconnect.io with the login on your seat card.
Devices, then Create Device. Fill in the four fields on the right.
Save & View.
Download the certificate package and unzip it.
Open both PEM files in a plain-text editor.
Field | Value
Unique ID | Your Device ID, e.g. ek-ra8p1-07
Entity | The workshop entity (only one)
Template | RA8P1 Vision AI (ra8p1vis)
Device Certificate | Auto-generated
Use exactly this template. It enables video streaming, and the platform provisions the video channel at the moment the device is created.
Checkpoint: your device is in the list as Disconnected, and the certificate and the private key are open in a text editor. Not Word.
EK-RA8P1 · /IOTCONNECT workshop
Notes: The template must be exactly RA8P1 Vision AI. It enables video streaming, and the platform provisions the video channel when the device is created; a device made from any other template will never stream in Lab 6. Auto-generated certificates are the easy path: the platform makes the key pair and you download both halves. Word, Pages and rich-text editors replace quotes and line endings, and the board rejects the paste; Notepad, TextEdit in plain-text mode, or VS Code are fine.

## Slide 12: Lab 3: Provision the board (15 min)
YOU TYPE, IN THE SERIAL TERMINAL
set env <ENV>
set cpid <CPID>
set duid ek-ra8p1-07
set cert then paste the certificate
set key then paste the private key
show
apply
THE BOARD PRINTS, WITHIN 30 SECONDS
IOTC: starting (env=... duid=ek-ra8p1-07,
credentials: stored)
IOTC: time synced
FU: file upload ready
IOTC: connected
FU: selftest creds fetch -> 0 (OK)
One PEM block per paste, from a plain-text editor. The board replies ok, certificate stored and private key stored.
Checkpoint: IOTC: connected on the console, the device shows Connected in the browser, and Live Data updates every 10 seconds. The board reconnects by itself from now on.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Say this before they start: certificate first, then the key, two separate pastes, each from BEGIN to END inclusive. The board says ok after each set, certificate stored and private key stored after the pastes, and show lets you check everything except the key, which is redacted. If a paste is rejected as too large, both files went in at once. ENV and CPID are on the seat card; the DUID is the Device ID you just created. After apply, the board fetches time over SNTP, discovers its endpoint, fetches file-upload credentials, and connects over MQTT with mutual TLS. All of this is stored in the board's flash: from now on it connects at every boot without a console.

## Slide 13: Lab 4: Dashboard, first push, snapshot (20 min)
4a Import the dashboard
Create Dashboard, then Import Dashboard. File ra8p1-vision-ai-dashboard.json, template RA8P1 Vision AI, device: yours. Name it Seat NN. Save.
4b Push Face Detect
AI Models, RA8P1 Face Detect, Deploy, select your device only. Watch the console. Step in front of the camera.
4c Take Snapshot
Press Take Snapshot on the dashboard. About 10 seconds later the Latest Snapshot widget shows the photo with the detection box drawn on it.
IOTC: model downloaded (441248 bytes)
FD: hot-swapping to model "face-v3" v3 (441088 bytes)
FD: model "face-v3" v3 (cloud, 441088 bytes) loaded: face detector, ethos-u: yes
FD: model persisted to OSPI flash store
Checkpoint: Active Model reads face-v3, inference is about 5,800 µs, Uptime never reset, and a snapshot with a box around your face is on your dashboard.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Do 4b on the big screen first, with your own board and console visible, then let them go. Deploy to your own device only: check the device ID in the dialog before you click. The four console lines are the whole story: download over HTTPS, hot-swap between two inferences, load, persist. The snapshot is worth a sentence: the board draws the boxes, encodes the PNG and signs the S3 upload itself, with AWS SigV4 computed on the microcontroller. On a headless install that image is the viewfinder. When most of the room has a box on a face, call the break.

## Slide 14: Your dashboard once the face detector is loaded
Detection State card switches between FACE, CLEAR, PERSON, NO PERSON and CLASSIFYING as the model changes.
Model Source card says where the running model came from: cloud after a push, flash after a power cycle.
NPU Inference Time chart is the model-swap history. Every push is a step in this line.
Uptime tile must never reset today. It is the proof that nothing rebooted.
EK-RA8P1 · /IOTCONNECT workshop
Notes: This screenshot is from a build with a built-in model, so its Model Source card says BUILT-IN; yours will say the model came from the cloud. Walk the room through the widgets that prove the claims: the state card for what the model sees, the source card for where the model came from, the inference-time chart for the history of swaps, and the Uptime tile that must never reset today. The command panel at the bottom right is where Take Snapshot, Model Revert and Send Command live.

## Slide 15
Break
10 minutes. Leave your board powered and connected.
When we return: what actually happened when you clicked Deploy.
Notes: Helpers use the break to clear anyone still short of the Lab 4 checkpoint, handing out a pre-provisioned spare board where needed. Boards stay powered so nobody loses their place.

## Slide 16: Anatomy of a model push
1
Deploy
AI Models sends a command over MQTT carrying a signed download URL.
2
Download
HTTPS from S3 into a 4 MB pending buffer in SDRAM, three retries on error.
3
Validate
Envelope header: magic, length, CRC32. Then a trial load checks the input shape.
4
Hot-swap
Between two inferences: tear down the interpreter, rebuild it over the same arena.
5
Persist
The envelope is written to a raw OSPI flash slot and reloaded at every boot.
A failure at step 3 or 4 keeps the previous model running. The camera, display and telemetry never stop during any step.
A push during a live video stream is deferred until the download can share the heap, then proceeds with the stream still playing.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Now that they have done it, the mechanism. One: the deploy is an ordinary cloud-to-device command on the MQTT session the board already holds, with a pre-signed URL for the file. Two: a second TLS session downloads it into SDRAM, not into the running model's memory; transient errors retry three times. Three: the envelope is checked, magic, length, CRC, and a trial load reads the input tensor shape to decide which family the model is. Four: the AI thread swaps between two inferences: destroy the TensorFlow Lite Micro interpreter, construct a new one over the same tensor arena with the new flatbuffer. Five: the envelope goes to a raw slot in external flash, which is what the board reads first next time. The safety property is the first grey box: any failure leaves the previous model running.

## Slide 17: What is inside the file you push
STORED ZIP, NO COMPRESSION
IOTV header, 32 bytes
magic IOTV · format version · model version · payload length · CRC32 · display name (15 chars)
Vela-compiled .tflite flatbuffer
The whole network as one ethos-u custom op carrying the NPU command stream. Made by tools/pack_model.py.
THE BOARD DETECTS THE FAMILY FROM THE INPUT TENSOR
Input shape | Treated as
192 × 192 × 1 | Face detector, two YOLO output heads, boxes
96 × 96 × 1 | Two-class classifier: person / no person
224 × 224 × 3 | 1000-class ImageNet classifier, top label
Limits: 4 MB enveloped, 640 KiB tensor arena (Vela's Total SRAM used), only the ops linked into this build. Anything else is rejected at load and the previous model restored.
EK-RA8P1 · /IOTCONNECT workshop
Notes: The file is a zip because that is what the AI Models upload takes, and it is a STORED zip because the board walks it in place with no inflate code. Inside is a 32-byte envelope and the model. The envelope carries the name and version the dashboard shows, and the CRC the board checks before it trusts the payload. The payload is the Vela output: Vela takes a quantized TensorFlow Lite model and rewrites everything the Ethos-U55 can run into a single custom op with the NPU's command stream, which is why both shipped families run entirely on the NPU. The table is the contract: the board looks at the input tensor shape to decide what kind of model it just received, so the same firmware runs three tasks with no configuration.

## Slide 18: The model library, already registered for you
In AI Models | What the board becomes | Input | Inference | Size
RA8P1 Face Detect | Face detector with boxes (YOLO Fastest) | 192×192 gray | 5.8 ms | 441 KB
RA8P1 Person Detect | Occupancy sensor: person present or absent | 96×96 gray | 1.5 ms | 240 KB
RA8P1 ImageNet Classifier 0.25 | 1000-class classifier, speed tier | 224×224 RGB | 4.5 ms | 432 KB
RA8P1 ImageNet Classifier 0.5 | 1000-class classifier, mid tier | 224×224 RGB | 9 ms | 1.1 MB
RA8P1 ImageNet Classifier v2 | 1000-class classifier, accuracy tier | 224×224 RGB | 40 ms | 3.1 MB
The camera delivers a frame every 18 ms. Every model here is faster than that: the NPU is never the bottleneck, even at 40 ms with frame skipping.
Classifier v2 is roughly seven times the face detector's size and workload. That is the one to push while you watch the inference chart.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Five models, three tasks, one firmware. The names in the first column are exactly what you will see in the deploy list. Inference times are measured on this hardware. The spread from one and a half milliseconds to forty is what makes the inference-time chart on the dashboard interesting: each push is a visible step. The face detector at 5.8 ms uses about a third of the NPU's time budget at 55 fps, which is why the seven-times-larger classifier can be absorbed without disturbing the camera or the display.

## Slide 19: Lab 5: Re-task the device from the cloud (30 min)
5a
Deploy ImageNet Classifier v2 (3.1 MB). Hold up a mug, a banana, a bottle. Watch the inference chart step to about 40 ms and Uptime keep counting.
5b
Deploy Person Detect. Walk out of frame and back. PERSON PRESENT, NO PERSON, inference about 1.5 ms.
5c
Send Model Info from the dashboard. The acknowledgment names the model, version, source and size.
5d
Unplug USB, count to three, plug it back in. No reprovisioning. The boot log says the model loaded from flash and the board reconnects.
5e
Deploy Face Detect again. The boxes come back. Time left? Push the 0.25 and 0.5 classifiers and compare the chart.
WATCH
FD: model "mobilenet-v2" v1 (cloud,
3152368 bytes) loaded: classifier
FD: model "person-detect" v1 (flash,
240272 bytes) loaded: classifier
IOTC: starting (credentials: stored)
IOTC: connected
The word flash in place of cloud after the power cycle, the Model Source card changing to match, and an Uptime tile that never went to zero during the swaps.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Push the classifier on your own board first and hold up a mug on the big screen, then let them go. Expect confidence between thirty and sixty percent: that is a softmax over a thousand classes, and the label being right is the point. Single objects, centred, close to the lens; ImageNet does not know scenes. Do 5d together as a room: everybody unplugs, counts to three, plugs in, and watches for the word flash. That is the applause moment. Model Revert on the dashboard clears the stored model rather than restoring a built-in one, because this image has none; after a revert inference idles until the next push.

## Slide 20: Three numbers that prove it
7×
larger model, absorbed live
Face detector at 5,800 µs to Classifier v2 at 40,000 µs, downloaded and swapped while the camera and display kept running.
0
reboots across every swap
The Uptime tile counts through the whole lab. The only time it resets is the power cycle you chose to do.
3
tasks, one firmware image
Face detection, occupancy sensing, 1000-class classification. The family is chosen by the model's input shape, not by a build flag.
And after the power cycle: the same model, from the board's own flash, in about 30 seconds, with no console attached.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Use this slide to close Lab 5 once most of the room has done the power cycle. Each number is something they saw on their own dashboard in the last half hour, not a claim from a datasheet. The seven-times figure is the workload jump between the face detector and Classifier v2. Zero reboots is the Uptime tile. Three tasks is the same firmware that was flashed yesterday. If anyone asks about fleet scale: every board in this room did this at the same time from the same AI Models entry.

## Slide 21: Lab 6: Live video, and a push mid-stream (10 min)
Open your device, select the Video Streaming tab.
Start Video. Allow 15 seconds. Black? Stop, then Start once more.
Wave at the camera. A second or two of latency is the relay.
With the video playing, deploy a different model.
Watch the stream stay up while the task changes. Stop Video.
No video hardware on this chip. H.264 is encoded in software on the Cortex-M85 at 320×240, about 8 to 10 frames per second.
Real WebRTC. Kinesis Video Streams signaling, ICE and TURN traversal, DTLS-SRTP encryption, negotiated on the microcontroller. One viewer per device.
Everything at once. The NPU keeps running inference on the same frames, telemetry keeps flowing, and a second TLS session downloads the model.
Checkpoint: you saw the live view, the console printed [KVSMedia] streaming ON, and the model changed while the video played.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Only run this as a lab if the day-before test on the venue network streamed successfully; otherwise demonstrate from the presenter board and move on. The first session after a boot can time out during TURN allocation, hence Stop and Start. The closer is step four: a model push while the stream is live. The board defers the download until the heap can hold both sessions, then downloads, validates and swaps with the video still playing. Two TLS sessions, a WebRTC session, the NPU and the camera, concurrently, on one microcontroller.

## Slide 22: Bring your own model
1
Quantize
Export an int8 TensorFlow Lite model whose input matches one of the three contracts.
2
Compile with Vela
Target ethos-u55-256. If Total SRAM used exceeds 640 KiB, recompile with the Size optimisation.
3
Pack
tools/pack_model.py wraps it in the IOTV envelope and writes the STORED zip.
4
Upload and push
AI Models, Create Model, Variant Renesas, upload the zip. Deploy to one device, then to the fleet.
pip install ethos-u-vela
vela --accelerator-config=ethos-u55-256 --optimise Performance --config <default_vela.ini> --memory-mode=Shared_Sram --system-config=Ethos_U55_High_End_Embedded model_quant.tflite
python tools/pack_model.py model_quant_vela.tflite --version 1 --name my-model
Limits: 4 MB enveloped, 640 KiB arena, only the ops linked into this build. A model with an unsupported shape is rejected on the device and the previous model restored.
EK-RA8P1 · /IOTCONNECT workshop
Notes: The path from your own network to a deploy button. Quantize to int8 with an input of 192 by 192 gray for a detector, 96 by 96 gray for a two-class classifier, or 224 by 224 RGB for an ImageNet-style classifier. Vela is Arm's compiler for the Ethos-U; the accelerator config is the 256-MAC U55 in the RA8P1. If Vela reports more than 640 KiB of SRAM, recompile for size; MobileNet v2 went from 1474 KiB to 353 KiB that way. pack_model.py is thirty lines of Python in the repository. Then AI Models, Create Model, upload, deploy.

## Slide 23: Where to go next
Quickstart
Repeat today at home on your own trial account, from unboxing, with the prebuilt image and no toolchain.
Developer Guide
Build from source with e² studio and FSP, the thread architecture, the memory budget, and adding your own models.
Demo Guide
A ten-minute presenter's script for showing the hot-swap to your own team, with expected results at every step.
The repository
github.com/avnet-iotconnect/iotc-freertos-ek-ra8p1: firmware, prebuilt image, template, dashboard, models, and these workshop materials.
The kit
EK-RA8P1 Evaluation Kit from Renesas: board, OV5640 camera, 7-inch LCD, cables. Search for EK-RA8P1 on renesas.com.
/IOTCONNECT trial
A free trial on the AWS backend at subscription.iotconnect.io, or 60 days through the AWS Marketplace.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Everything on this slide is in the repository's README. The Quickstart is today's flow written for one person at home, including creating the trial account. The Developer Guide is where the vendor patches, the memory budget and the model contracts live. Point people at the repository URL on the whiteboard rather than reading it out.

## Slide 24: Before you leave
The board stays here
In the serial console type erase, then reboot. The board forgets its identity. Leave it, the cables and your seat card on the desk.
The board goes home with you
Leave it provisioned tonight. This account closes after the event, so follow the Quickstart to make your own, then erase, reboot and provision again.
Thank you. You pushed three models to a microcontroller today, and it never rebooted.
EK-RA8P1 · /IOTCONNECT workshop
Notes: Say which of the two cards applies before anyone stands up. If boards are collected, the erase matters: a provisioned board is a live identity in the workshop account. If boards go home, remind people the account is temporary and the Quickstart covers the rest. Collect seat cards either way; they carry a login.

## Slide 25
Notes: Questions. The repository URL and the guides are on the whiteboard.